## Slide 1
IoT AND APPLICATIONS
Module 1
Introduction to IoT Technology
Contact Hours: 9 | CO1 (K2): Understand IoT fundamentals and architecture modelling
JECC | S5 | PEMRT525
[TB1] Bahga & Madisetti
[TB2] Cisco Press
[TB3] Raj Kamal
[REF1] Al-Fuqaha et al.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 2
MODULE OVERVIEW
Topics Covered in Module 1
1
Definitions & Characteristics of IoT
1.5 hrs
2
IoT Architectural View (3-layer, 5-layer, CISCO 7-level)
1.5 hrs
3
Physical Design of IoT
1.0 hr
4
Logical Design — IoT Functional Blocks
1.5 hrs
5
IoT Communication Models
1.0 hr
6
IoT Enabling Technologies
1.5 hrs
7
IoT Levels & Deployment Templates
1.0 hr
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 3
TOPIC 1: DEFINITIONS
What is the Internet of Things?
IoT Equation (McEwen): Physical Object + Controller / Sensor / Actuator + Internet = Internet of Things
[TB3] Raj Kamal, p.2
"A network of physical things sending, receiving, or communicating information using the Internet, enabling monitoring, coordinating or controlling across the network."
[TB2] Cisco Press, Ch.1
"A technology transition in which devices allow us to sense and control the physical world. The basic premise of IoT is to connect the unconnected."
[REF1] Al-Fuqaha et al., IEEE 2015
"The IoT enables physical objects to see, hear, think and perform jobs by having them talk together — transforming traditional objects into smart objects."
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 4
TOPIC 1: VISION
IoT Vision & Conceptual Frameworks
Vision: Everyday things become "smart" — sensing, computing, communicating through embedded devices, interacting with remote systems and people via Internet or NFC. [TB3, p.3]
🌂 Smart Umbrella [TB3, pp.3-4]
Embedded circuit connects to weather website each morning. Analyses forecast. Alerts owner: RED LED = hot/sunny, YELLOW LED = rainy. Sends SMS to mobile. No human involvement needed.
💡 Smart Streetlights [TB3, Fig.1.1]
32 streetlights per group connect to controller via ZigBee. Controller links to central station via Internet. Station monitors faults, traffic, ambient light and remotely programs controllers.
McEwen
Object + Sensor/Controller + Internet = IoT
Single device scale
Oracle
Gather → Enrich → Stream → Manage → Acquire → Organise & Analyse
Multi-device enterprise
IBM
Gather → Consolidate → Connect → Collect → Assemble → Manage & Analyse
IBM Cloud IoT platform
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 5
TOPIC 1: CHARACTERISTICS
Characteristics of IoT Systems
Dynamic &
Self-Adapting
Changes behaviour automatically based on context — no human intervention. [TB3; REF1]
Self-
Configuring
Devices configure themselves for network operation — plug-and-play. [TB3]
Interoperable
Protocols
Uses standard protocols (MQTT, CoAP, HTTP, ZigBee) for cross-manufacturer compatibility. [REF1]
Unique
Identity
Each device has a globally unique ID — IPv6 address or RFID/EPC code. [TB3, p.2]
Large-Scale
Deployment
50 billion+ devices by 2020. Requires scalable IPv6 and cloud infrastructure. [TB2]
Sensing &
Actuation
Sensors measure physical parameters; actuators perform physical actions. [TB3, p.14]
Ubiquitous
Data Exchange
"Anywhere, anytime" connectivity — continuous data exchange. [REF1]
Embedded
Intelligence
Local MCU + AI/ML for autonomous decisions without cloud round-trip. [TB2]
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 6
TOPIC 2: ARCHITECTURE
Three-Layer IoT Architecture
APPLICATION LAYER
Smart home apps • Healthcare dashboards • Industrial SCADA • City control systems
NETWORK LAYER
Wi-Fi (802.11) • 4G/5G • ZigBee • BLE • LoRa • Ethernet • TCP/IP • IPv6 • Gateways
PERCEPTION LAYER
DHT11 • PIR sensor • GPS • Accelerometer • RFID • Relay • DC motor • Solenoid valve
← Data Flow
(Perception to Application)
Command Flow →
(Application to Actuators)
[TB3] Raj Kamal, Ch.1, pp.9-12 | Source: Raj Kamal "Internet of Things: Architecture and Design Principles", McGraw Hill, 2022
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 7
TOPIC 2: ARCHITECTURE
Five-Layer & CISCO Seven-Level Architecture
Five-Layer Architecture
5. Business Layer
Strategic management & business decisions
4. Application Layer
Domain-specific apps (smart home, healthcare)
3. Processing Layer
Cloud, databases, big data analytics (Hadoop, Spark)
2. Transport Layer
Wi-Fi, 4G, ZigBee, Ethernet, BLE
1. Perception Layer
Sensors & actuators
CISCO 7-Level Reference Model [TB3, Fig.1.4]
L7
Collaboration & Processes
Business workflow
L6
Application
Reporting & control
L5
Data Abstraction
Aggregation & access
L4
Data Accumulation
Storage
L3
Edge Computing
Local data analysis
L2
Connectivity
Gateways & routers
L1
Physical Devices
Sensors & controllers
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 8
TOPIC 3: PHYSICAL DESIGN
Components of an IoT Node [TB3, Raj Kamal, Fig.1.6]
MCU / PROCESSOR
Processor Core
RAM | Flash
Timers | UART
SPI | I2C | GPIO
ADC | PWM
SENSORS
Analog: Thermistor, LDR, Pressure
Digital: PIR, Touch, Proximity
[TB3, p.14]
ACTUATORS
DC Motor, Servo Motor
Relay, Solenoid Valve
LED, Buzzer, LCD
COMM MODULE
Wi-Fi (ESP8266/ESP32)
ZigBee (XBee)
BLE, LoRa, 4G, NFC
[TB3, p.15]
POWER UNIT
Li-ion / LiPo battery
Solar panel + MPPT
Mains 3.3V / 5V
Energy harvesting
OS / FIRMWARE
RIOT OS | Contiki | FreeRTOS | Raspbian [TB3, p.15]
→ Internet
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 9
TOPIC 3: PLATFORMS
Popular IoT Development Platforms [TB3, §1.5, pp.19-21]
Arduino Yún
ATmega32u4 + Atheros AR9331 Linux module
Wi-Fi, Ethernet, USB, micro-SD
12 analog + 20 digital I/O
Raspberry Pi
ARM-based Linux SBC (Raspbian OS)
40-pin GPIO (UART, SPI, I2C)
USB, HDMI, Ethernet, Camera port
BeagleBone Black
ARM Cortex-A8, 512 MB RAM
46 GPIO, 7 analog, 2 SPI, 2 I2C
Runs Android & Linux. Low power.
Intel Galileo/Edison
Arduino-certified, Intel x86 Quark SoC
20 digital I/O, 12-bit PWM
6 analog inputs, UART, SPI, I2C
ESP32 / NodeMCU
Dual-core 240 MHz, 4 MB Flash
Integrated Wi-Fi + BLE/Bluetooth
34 GPIO, ADC, DAC, Touch pins. ~₹350
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 10
TOPIC 4: LOGICAL DESIGN
IoT Functional Blocks [TB1, Bahga & Madisetti, Ch.1]
APPLICATION
SERVICES
COMMUNICATION
MANAGEMENT
RESOURCE (Device APIs / Firmware)
DEVICE (Sensors + Actuators + Local Control)
SECURITY BLOCK — Authentication | Authorisation | Encryption (TLS/DTLS) | Data Integrity (Cross-cutting across all blocks)
Device:
Physical node — senses & actuates the physical world.
Resource:
Firmware APIs exposing device functions to network.
Communication:
MQTT / CoAP / HTTP — device-to-cloud data exchange.
Services:
Device monitoring, data publish/subscribe, discovery.
Management:
OTA updates, remote config, fault management.
Application:
Dashboard, analytics, remote control for end users.
Security:
Auth, encryption, integrity — protects all other blocks.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 11
TOPIC 5: COMM MODELS
IoT Communication Models [TB1; REF1, Al-Fuqaha et al.]
1. Request-Response
Client ──[Request]──▶ Server
Server ──[Response]──▶ Client
Sync | HTTP, CoAP
Best for: On-demand queries
Limit: Polling overhead
2. Publish-Subscribe
Publisher ──[topic]──▶ BROKER
BROKER ──[fan-out]──▶ Subscribers
Async | MQTT, AMQP
Best for: Real-time streaming
Limit: Needs broker
3. Push-Pull
Producer ──[push]──▶ QUEUE
QUEUE ──[pull]──▶ Consumer
Async | Kafka, RabbitMQ
Best for: Data pipelines
Limit: Queue latency
4. Exclusive Pair
Client ◀══[full-duplex]══▶ Server
(Persistent TCP connection)
Sync | WebSocket
Best for: Interactive control
Limit: Stateful, hard to scale
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 12
TOPIC 5: MQTT
MQTT — The Primary IoT Messaging Protocol [REF1; TB3, Ch.3]
What is MQTT?
Message Queue Telemetry Transport
• Lightweight publish-subscribe protocol
• Runs over TCP/IP
• Minimum 2-byte fixed header
• Designed for constrained devices and unreliable, low-bandwidth networks
• Standardised by OASIS
• Default port: 1883 (8883 for TLS)
Quality of Service (QoS) Levels
QoS 0
At most once — fire and forget. No guarantee.
QoS 1
At least once — guaranteed delivery, possible duplicates.
QoS 2
Exactly once — guaranteed delivery, no duplicates.
Key Features
• Last Will & Testament (LWT): Broker notifies all subscribers if device disconnects abnormally.
• Retained Messages: Broker stores last message — new subscribers receive it immediately.
• Clean Session: Option to clear all subscriptions on reconnect.
• Keep-Alive: Heartbeat mechanism to detect broken connections.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 13
TOPIC 6: ENABLING TECH
IoT Enabling Technologies — Part 1 [TB3; REF1]
Wireless Sensor
Networks (WSN)
Network of autonomous sensor nodes monitoring physical conditions and cooperatively forwarding data to a sink/gateway.
Node = Sensing unit + MCU + Radio transceiver + Power unit.
Standard: IEEE 802.15.4
Routing: RPL protocol
Applications: Agriculture, environmental monitoring, structural health.
Cloud Computing
Scalable infrastructure for IoT data storage, processing, and analytics.
IaaS: AWS EC2, Azure VMs
PaaS: AWS IoT Core, Azure IoT Hub, IBM Watson IoT, ThingSpeak, Nimbits
SaaS: Ready-to-use analytics dashboards
ThingSpeak: Open platform with MATLAB analytics. Integrates with Arduino & RPi. [TB3, p.18]
Big Data Analytics
IoT generates massive data Volume, high Velocity, multiple Variety.
• Hadoop (HDFS + MapReduce): Batch processing of stored IoT data
• Apache Spark: In-memory stream analytics — 10-100× faster
• Apache Kafka: Real-time event streaming
• GROK (Numenta): Machine intelligence for IoT anomaly detection [TB3, p.13]
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 14
TOPIC 6: ENABLING TECH
IoT Enabling Technologies — Part 2 [TB3; REF1]
RFID & NFC [TB3, p.2; REF1]
RFID: Tag (passive/active) contains EPC code; reader detects wirelessly.
• Passive: Reader-powered. Range: 10 m. Freq: 125 kHz / 13.56 MHz / 860-960 MHz.
• Active: Battery. Range: 100 m. Asset tracking.
NFC: <20 cm, 13.56 MHz. Contactless payment, device pairing, access control.
Applications: Supply chain, inventory, library, animal tagging, tap-to-pay.
IPv6 & 6LoWPAN [TB3, p.13; REF1]
IPv4 exhausted (only 4.3B addresses). IPv6: 128-bit = 3.4×10³⁸ addresses.
6LoWPAN (RFC 4944): Bridges IPv6 with IEEE 802.15.4 (max 127-byte frames).
• Header Compression: 40-byte IPv6 → 2-3 bytes (95% reduction)
• Fragmentation: Splits large IPv6 packets into 802.15.4 frames
• Mesh Addressing: Multi-hop networking for WSN topologies
Embedded Systems
& Protocols [TB3, pp.14-18]
MCUs: ATmega328, ARM Cortex-M0/M3/M4, ESP32, STM32
RTOS: FreeRTOS, RIOT OS — deterministic real-time scheduling
Arduino: Open C/C++ platform — most popular for IoT prototyping
Eclipse IoT: Open-source MQTT, CoAP, OMA-LWM2M implementation
Protocols: MQTT, CoAP, HTTP, AMQP, XMPP, WebSocket [REF1, §V]
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 15
TOPIC 7: IoT LEVELS
IoT Deployment Levels 1–3 [TB1, Bahga & Madisetti, Ch.1]
1
Single Node
Local Analysis
[Node] → Local Analysis → Actuator
(no Internet required)
Key Feature:
Single device, all intelligence on-board. No cloud.
Example:
Standalone thermostat — senses temperature, controls HVAC relay directly.
2
Single Node
Cloud Analysis
[Node] → Internet → [Cloud] → [Dashboard]
Key Feature:
Single device. Data sent to cloud for analysis and storage.
Example:
Home weather station uploading temperature to ThingSpeak every 5 minutes.
3
Single Node
Cloud + Big Data
[Node] → [Cloud] → [Hadoop/Spark/ML] → [Insights]
Key Feature:
Single node. Cloud runs big data analytics and machine learning.
Example:
Industrial vibration sensor → AWS Spark ML predicts bearing failure 72 hrs ahead.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 16
TOPIC 7: IoT LEVELS
IoT Deployment Levels 4–6 [TB1, Bahga & Madisetti, Ch.1]
4
Multi-Node
Cloud Analysis
[Node 1] ─┐
[Node 2] ─┼─▶ [Cloud] ─▶ [App]
[Node N] ─┘
Key Feature:
Multiple independent nodes, each connecting directly to cloud. No gateway.
Example:
Smart parking: each bay sensor reports to cloud independently. Cloud shows availability.
5
Multi-Node +
Gateway + Cloud
[Nodes] ─ZigBee─▶ [Gateway] ─Internet─▶ [Cloud] ─▶ [App]
Key Feature:
Nodes use ZigBee/BLE to gateway. Gateway aggregates and pre-processes before cloud upload.
Example:
Agricultural WSN: 50 soil sensors → ZigBee → RPi gateway → hourly averages to cloud.
6
Multi-System
Smart City Scale
[Traffic Cloud]─┐
[Energy Cloud] ─┼─▶ [Central Cloud + Big Data] ─▶ [Dashboard]
[Water Cloud] ─┘
Key Feature:
Multiple independent IoT systems with own clouds, integrated by a central big data platform.
Example:
Smart city: traffic + energy + water + safety IoT systems integrated for city-wide analytics.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 17
TOPIC 7: SUMMARY
IoT Levels — Quick Comparison [TB1, Bahga & Madisetti]
Level
Name
Nodes
Analysis
Cloud?
Example
L1
Single Node, Local
1 node
On-device
No
Standalone thermostat
L2
Single Node + Cloud
1 node
Cloud
Yes
Home weather station
L3
Single + Big Data
1 node
Cloud + ML
Yes
Industrial vibration monitor
L4
Multi-Node + Cloud
Multiple
Cloud
Yes
Smart parking
L5
Multi-Node + Gateway
Multiple + GW
Gateway + Cloud
Yes
Agricultural WSN
L6
Multi-System City
Multi-systems
Central + Big Data
Yes
Smart city platform
Key Insight: L1→L2 (add cloud) | L2→L3 (add big data) | L3→L4 (add more nodes) | L4→L5 (add gateway) | L5→L6 (add system integration)
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 18
TOPIC 6: PROTOCOLS
IoT Communication Protocols Compared [REF1, Al-Fuqaha et al.; TB3, Ch.3]
Protocol
Transport
Overhead
QoS
Best Use Case
MQTT
TCP/IP
Very Low (2B header)
0, 1, 2
Sensor streaming, home automation
CoAP
UDP
Very Low
0 (NON), 1 (CON)
Constrained devices (8-bit MCUs)
HTTP/REST
TCP/IP
High
N/A
Web-capable devices, APIs
AMQP
TCP/IP
Medium-High
Yes
Enterprise IoT, financial sector
XMPP
TCP/IP
Medium
N/A
Presence-aware IoT systems
WebSocket
TCP/IP
Low (after handshake)
N/A
Real-time control dashboards
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 19
EXAM PREP
Expected Examination Questions — Part A (3 Marks Each)
1
Define IoT. List any four characteristics with examples.
2
State the four IoT communication models and the protocol used in each.
3
What is 6LoWPAN? Why is it needed for IoT?
4
Differentiate between Request-Response and Publish-Subscribe models.
5
Name the seven IoT functional blocks (Bahga & Madisetti).
6
Compare IoT Level 1 and Level 2 with examples.
7
What is MQTT? State any three key features.
8
Name any four IoT enabling technologies with one-line descriptions.
9
Differentiate between physical design and logical design of an IoT system.
10
What is a WSN? What is the role of the gateway node?
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 20
EXAM PREP
Expected Examination Questions — Part B (9 Marks Each)
Q1
Explain the IoT Architectural View with neat diagrams. Compare 3-layer and 5-layer architectures. Also describe the CISCO 7-level model.
Q2
Describe all seven IoT functional blocks with a block diagram and examples for each.
Q3
Explain the four IoT communication models with diagrams. For each, state protocol, working, and application.
Q4
Describe IoT enabling technologies: WSN, Cloud Computing, Big Data Analytics, RFID, IPv6/6LoWPAN, and Embedded Systems.
Q5
Explain IoT Levels 1 to 6 with diagrams and examples. State the key difference between each consecutive level.
Q6
Describe the physical design of an IoT system. Explain each hardware component with a diagram. List four development platforms.
Q7
Explain the characteristics of IoT in detail with real-world examples for each characteristic.
Q8
Explain IoT definitions from three textbook perspectives, the IoT vision with examples, and the three conceptual framework equations.
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 21
REFERENCES
Prescribed Textbooks & Reference Materials
[TB1]
Bahga, A. & Madisetti, V. — "Internet of Things: A Hands-on Approach", VPT, 2014
Used for: Functional Blocks, Communication Models, IoT Levels 1-6
[TB2]
Hanes, Salgueiro et al. — "IoT Fundamentals: Networking Technologies, Protocols & Use Cases", Cisco Press, 2017
Used for: IoT Definition, Architecture, Smart Objects, MQTT
[TB3]
Raj Kamal — "Internet of Things: Architecture and Design Principles", McGraw Hill India, 2nd Ed., 2022
Used for: Definitions, Frameworks, Architecture, Physical Design
[TB4]
Simon Monk — "Raspberry Pi Cookbook: Software and Hardware Problems and Solutions", O'Reilly/SPD, 2016
Used for: Raspberry Pi hardware interfacing
[REF1]
Al-Fuqaha, Guizani et al. — "Internet of Things: A Survey on Enabling Technologies, Protocols & Applications", IEEE Commun. Surveys & Tutorials, Vol.17, No.4, 2015
Used for: Enabling Technologies, Protocols, WSN, 6LoWPAN
IoT and Applications | PEMRT525 | S5 | JECC

## Slide 22
MODULE 1 COMPLETE
Introduction to IoT Technology
✓ IoT Definitions & Characteristics
✓ 3-Layer, 5-Layer, CISCO 7-Level Architecture
✓ Physical Design — IoT Node Components
✓ Logical Design — 7 Functional Blocks
✓ 4 Communication Models (MQTT, CoAP, WebSocket)
✓ 6 Enabling Technologies (WSN, Cloud, RFID, 6LoWPAN)
✓ IoT Levels 1–6 & Deployment Templates
Refer to Study Notes
Module1_Complete_Study_Notes.docx
github.com/jineshkjose/
IoT-Applications-PEMRT525
IoT and Applications | PEMRT525 | S5 | JECC