## Slide 1
PEMRT525 | Semester S5
IOT AND APPLICATIONS
MODULE 1
Introduction to IoT Technology
Definitions & Characteristics • Architecture • Physical & Logical Design • Communication Models • Enabling Technologies • IoT Levels
Contact Hours: 9 Hrs | CO1: K2 – Understand IoT Fundamentals
Notes: Welcome slide. Introduce the course and module. Total 4 modules, 36 hours. Module 1 covers IoT fundamentals – the foundation for all subsequent modules.

## Slide 2
MODULE OVERVIEW
What We Cover in Module 1
IoT and Applications (PEMRT525) | Module 1 | S5
2
1
Definitions & Characteristics
What is IoT? Key properties of IoT systems.
2
IoT Architectural View
3-layer and 5-layer architecture models.
3
Physical Design of IoT
IoT node components and hardware.
4
Logical Design & Functional Blocks
7 functional blocks of an IoT system.
5
IoT Communication Models
Request-Response, Pub-Sub, Push-Pull, Exclusive Pair.
6
IoT Enabling Technologies
WSN, Cloud, RFID, IPv6, Embedded Systems.
7
IoT Levels & Deployment Templates
6 deployment levels with examples.
Notes: Give students the roadmap. 9 hours = ~1.5 hrs per major topic. Emphasize that Module 1 is the foundation – if this is clear, all other modules build on it easily.

## Slide 3
TOPIC 1
What is the Internet of Things?
IoT and Applications (PEMRT525) | Module 1 | S5
3
Definition (Bahga & Madisetti):
A paradigm in which everyday objects are equipped with unique identifiers and connectivity, enabling them to collect, exchange, and act on data with minimal human intervention.
75 Billion
Connected devices by 2025 (Statista)
$1.1 Trillion
Projected IoT market value (2026)
Three Pillars of IoT
Things
Physical objects with sensors embedded in the environment.
Connectivity
Network links enabling data to flow between things and systems.
Intelligence
Analytics and AI that transform raw data into useful actions.
Notes: Ask students: what objects in their home could be 'smart'? Fridge, AC, water meter, door lock. Each one = a 'Thing'. When networked + smart = IoT.

## Slide 4
TOPIC 1
Key Characteristics of IoT
IoT and Applications (PEMRT525) | Module 1 | S5
4
Dynamic & Self-Adapting
Adapts to context; e.g. smart thermostat learns patterns.
Self-Configuring
Plug-and-play; automatic firmware updates.
Interoperable
Standard protocols (MQTT, CoAP) across manufacturers.
Unique Identity
Every device has a unique ID (IPv6, EPC) for tracking.
Large Scale
Billions of devices; needs scalable infrastructure.
Sensing & Actuation
Sense environment and perform physical actions.
Ubiquitous Data Exchange
Continuous data flow between devices and cloud.
Notes: Go through each characteristic with a real-world example. Ask students to match each characteristic to a device they know. Dynamic = Nest thermostat. Unique Identity = Your Aadhaar card has a unique number – same concept.

## Slide 5
TOPIC 2
IoT Architectural View – 3-Layer Model
IoT and Applications (PEMRT525) | Module 1 | S5
5
Application Layer
Smart Home • Healthcare • Agriculture • Smart City
Network Layer
Wi-Fi • 4G/5G • ZigBee • LoRa • Bluetooth
Perception Layer
Temperature Sensor • GPS • RFID Tag • Camera • Actuator
1
Delivers application-specific services to end users via dashboards and apps.
2
Transmits data from devices to processing systems. Handles routing and security.
3
Physical layer: senses the environment and collects raw data from the physical world.
Data Flow ↑↓
Notes: Draw this on the board. Ask: A temperature sensor in a greenhouse → which layer? (Perception). The data it sends via Wi-Fi → which layer? (Network). The mobile app showing temperature → which layer? (Application).

## Slide 6
TOPIC 2
IoT Architectural View – 5-Layer Model
IoT and Applications (PEMRT525) | Module 1 | S5
6
Business Layer
Business models, flowcharts, analytics output for management decisions.
Application Layer
Manages specific IoT applications: smart city, healthcare, agriculture.
Processing Layer (Middleware)
Stores, analyses, and processes data. Uses cloud, big data, databases.
Transport Layer
Transmits data between perception and processing via Wi-Fi, 4G, etc.
Perception Layer
Physical sensors and actuators collecting real-world data.
Key difference from 3-layer: adds Processing (Middleware) layer and Business layer for enterprise-grade IoT deployments.
Notes: The 5-layer model is more relevant for industrial and enterprise IoT. The extra layers (Processing/Middleware and Business) handle the complexity of managing thousands of devices and making business decisions from data.

## Slide 7
TOPIC 3
Physical Design of IoT – Node Components
IoT and Applications (PEMRT525) | Module 1 | S5
7
1
Microcontroller
ESP32, ARM Cortex-M, Arduino Uno
2
Memory (RAM/Flash)
Stores program code & sensor data
3
Sensors
DHT11 (temp/humidity), PIR, LDR, GPS
4
Actuators
Motor, Relay, Servo, Buzzer, LED
5
Communication
Wi-Fi (ESP8266), BLE, ZigBee, LoRa
6
Power Source
Battery, Solar, Mains; Energy Harvesting
7
I/O Interface
GPIO, UART, SPI, I2C peripherals
Notes: If available, show a NodeMCU or Raspberry Pi board. Walk through each component physically. Students should be able to identify: where is the MCU? Where is the Wi-Fi chip? What sensor is connected?

## Slide 8
TOPIC 4
Logical Design of IoT
IoT Functional Blocks
1
Device
2
Resource
3
Communication
4
Services
5
Management
6
Security
7
Application
(Bahga & Madisetti model – next slide expands each block)
IoT and Applications (PEMRT525) | Module 1 | S5
8
Notes: The logical design describes WHAT the system does, not how the hardware is built. Seven functional blocks are abstract units of functionality present in any complete IoT system.

## Slide 9
TOPIC 4
IoT Functional Blocks – Details
IoT and Applications (PEMRT525) | Module 1 | S5
9
1
Device
Physical IoT node with sensing, actuation & control capabilities.
2
Resource
Software APIs and firmware providing hardware abstraction.
3
Communication
Connectivity between devices, gateways & cloud (MQTT, CoAP).
4
Services
Device monitoring, data publishing and subscription services.
5
Management
Device configuration, diagnostics and OTA firmware updates.
6
Security
Authentication, authorization, encryption and message integrity.
7
Application
User interface, dashboards, analytics and control portals.
Notes: Walk through each block with an example: if you were designing a smart electricity meter — which block handles the sensor reading? (Device) Which block exposes the reading via an API? (Resource) Which block sends the reading to the utility server? (Communication).

## Slide 10
TOPIC 5
IoT Communication Models
How IoT devices exchange data – 4 models defined by the Internet Architecture Board (IAB)
⇄
Request-Response
HTTP, CoAP
Analogy:
Telephone call
⊕
Publish-Subscribe
MQTT, AMQP
Analogy:
Newspaper subscription
⇩
Push-Pull
Kafka, RabbitMQ
Analogy:
Email inbox
⇔
Exclusive Pair
WebSocket
Analogy:
Video call
IoT and Applications (PEMRT525) | Module 1 | S5
10
Notes: Use analogies to make the models memorable. Request-Response = you call a friend, they answer (or not). Pub-Sub = you subscribe to a newspaper, it arrives every morning without you calling. Push-Pull = your email sits in the inbox until you open it. Exclusive Pair = you're on a live video call, both talking simultaneously.

## Slide 11
TOPIC 5
Communication Models – Detailed Comparison
IoT and Applications (PEMRT525) | Module 1 | S5
11
Model | Direction | Synchronous? | Protocol | Best For | Limitation
Request-Response | Client → Server → Client | Yes | HTTP, CoAP | On-demand queries | High overhead for frequent polling
Publish-Subscribe | Publisher → Broker → Subscribers | No (async) | MQTT, AMQP | Real-time data streams | Requires broker infrastructure
Push-Pull | Producer → Queue → Consumer | No (async) | Kafka, RabbitMQ | Data pipelines & batch | Latency depends on queue depth
Exclusive Pair | Bi-directional (persistent) | Yes (real-time) | WebSocket | Interactive control | Stateful; harder to scale
Notes: Focus on exam-relevant differences: MQTT is the dominant IoT protocol (pub-sub). HTTP is familiar from web – synchronous. WebSocket is real-time bidirectional. Students are expected to explain and compare these for ESE Part B.

## Slide 12
TOPIC 6
IoT Enabling Technologies
IoT and Applications (PEMRT525) | Module 1 | S5
12
◉
Wireless Sensor Networks (WSN)
Distributed sensor nodes collecting environmental data. Foundation of IoT data collection.
☁
Cloud Computing
Infrastructure for storing and processing IoT data at scale (AWS IoT, Azure IoT Hub).
∑
Big Data Analytics
Tools (Hadoop, Spark) for extracting insights from massive IoT data streams.
⚙
Embedded Systems
MCUs/MPUs (Arduino, ESP32, Raspberry Pi) running IoT firmware and RTOS.
📡
RFID & NFC
Wireless identification of objects. NFC = short range (<20 cm). RFID = inventory tracking.
IP
IPv6 / 6LoWPAN
IPv6 provides 3.4×10³⁸ addresses for every IoT device. 6LoWPAN = IPv6 over 802.15.4.
Notes: Draw a mind map connecting 'IoT System' → each enabling technology. Ask: a smart agricultural system that monitors soil moisture across 500 sensors – which technologies are used? (WSN + Cloud + Big Data + IPv6 + Embedded).

## Slide 13
TOPIC 7
IoT Levels – Deployment Complexity
IoT and Applications (PEMRT525) | Module 1 | S5
13
L1 | Single Node
Local sensing & analysis. No cloud. Standalone device.
e.g. Standalone thermostat
L2 | + Cloud
Node uploads data to cloud for storage and analysis.
e.g. Weather station → cloud
L3 | + Big Data
Cloud with big data analytics for large-volume processing.
e.g. Industrial vibration monitoring
L4 | Multi-Node + Cloud
Multiple sensors uploading to a single cloud.
e.g. Smart parking system
L5 | + Gateway
Nodes → coordinator (gateway) → cloud.
e.g. Agricultural WSN + gateway
L6 | Multi-System
Multiple independent systems with coordinated central cloud.
e.g. Smart city integration
Notes: Key exam point: be able to classify a given IoT system into one of the 6 levels. A Fitbit = Level 2 (syncs to phone) or Level 3 (cloud analytics). A smart city = Level 6. Ask: which level is your college's attendance system?

## Slide 14
TOPIC 7
IoT Deployment Templates
IoT and Applications (PEMRT525) | Module 1 | S5
14
Home Automation
Sensors → Local Gateway → Cloud → Mobile App
Smart Energy
Smart Meters → Aggregator → Utility Cloud → Analytics
Industrial IoT
Machine Sensors → Edge Gateway → Industrial Cloud → SCADA
Connected Health
Wearables → Smartphone Gateway → Healthcare Cloud → Doctor Dashboard
← Data Flows from Physical World to Cloud to Users →
Notes: Templates are reusable design patterns. Ask students to draw the architecture for a smart college campus monitoring attendance, electricity usage, and classroom occupancy – which template or combination of templates would they use?

## Slide 15
MODULE 1 SUMMARY
Key Takeaways
IoT = Things + Connectivity + Intelligence; 7 key characteristics distinguish IoT systems.
Architecture: 3-layer (Perception/Network/Application) or 5-layer (+ Processing + Business).
Physical design: MCU, sensors, actuators, communication module, memory, power, I/O.
7 Functional blocks: Device, Resource, Communication, Services, Management, Security, Application.
4 Communication models: Request-Response, Pub-Sub, Push-Pull, Exclusive Pair.
Enabling technologies: WSN, Cloud, Big Data, Embedded Systems, RFID, IPv6/6LoWPAN.
6 IoT levels from standalone device (L1) to multi-system smart city integration (L6).
IoT and Applications (PEMRT525) | Module 1 | S5
15
Notes: Recap all topics before the next class. Assign: Review the NPTEL Module 1 lectures at https://onlinecourses.nptel.ac.in/noc22_cs53/preview. Answer: What level is your smartphone's Google Maps navigation in the IoT levels model?

## Slide 16
ESE PREP
Exam Focus & References
IoT and Applications (PEMRT525) | Module 1 | S5
16
Part A – 3 Mark Questions
Q1. Define IoT. List 4 characteristics.
Q2. Name the 7 IoT functional blocks.
Q3. List the 4 IoT communication models.
Q4. What are IoT enabling technologies?
Q5. Differentiate Request-Response and Pub-Sub.
Q6. What is the difference between physical and logical design?
Part B – 9 Mark Questions
Q1. Explain 3-layer & 5-layer architecture with diagrams.
Q2. Explain all 7 functional blocks with a block diagram.
Q3. Describe the 4 communication models with diagrams.
Q4. Explain IoT enabling technologies.
Q5. Explain IoT levels 1–6 with examples.
Q6. Describe physical design: IoT node components.
References:
Bahga & Madisetti – Internet of Things (VPT, 2014, Ch.1-2) | Hanes et al. – IoT Fundamentals (Cisco Press, 2017) | Rajkamal – IoT: Architecture & Design Principles (McGraw Hill, 2022) | NPTEL: https://onlinecourses.nptel.ac.in/noc22_cs53/preview
Notes: Remind students: CIE = 40 marks (Attendance 5, Internal Exam 15, Evaluate 10, Analyse 10). ESE = 60 marks (Part A: 8×3=24, Part B: 4×9=36). Module 1 concepts appear in BOTH Part A and Part B.