## Slide 1
MODULE 2
Internet of Things
& Applications
IoT & M2M • SDN & NFV • Smart Objects • Sensor Networks
WSN Protocols • Communication Criteria
PEMRT525 | KTU | S5 | JECC
9 Contact Hours

## Slide 2
Module 2 — Topics at a Glance
01
M2M
Communication
02
IoT vs M2M
Differences
03
SDN & NFV
for IoT
04
Sensors &
Actuators
05
MEMS &
Smart Objects
06
Wireless Sensor
Networks (WSN)
07
Communication
Criteria
What You Will Learn
1
Understand M2M architecture and how it evolved into IoT
2
Grasp SDN/NFV for scalable, programmable IoT networks
3
Classify sensors, actuators, and MEMS devices
4
Analyse WSN design, constraints, and communication patterns
5
Apply communication criteria to select the right wireless technology

## Slide 3
M2M — Machine-to-Machine Communication
Definition: Direct data communication between machines/devices WITHOUT human intervention
M2M DEVICE
Field Domain
Sensors / actuators collect data and transmit wirelessly
Examples: Smart meters, vehicle trackers, vending machines
NETWORK
Communication
Carries data between devices and application
Examples: Cellular (2G/3G/4G), ZigBee, WiFi, Wired LAN
APPLICATION
Application Domain
Receives, processes & acts on data
Examples: SCADA, Cloud server, Analytics platform
►
►

## Slide 4
IoT vs M2M — Key Differences
Aspect
M2M
IoT
Architecture
Closed, proprietary networks
Open Internet standards (IP, cloud)
Communication
Point-to-point, device-to-server
Device-to-device, device-to-cloud
Intelligence
Data collection & transmission only
Analytics, AI/ML, real-time insights
Scalability
Limited — point solutions
Billions of devices — highly scalable
Standards
Proprietary, vendor-specific
Open: MQTT, CoAP, HTTP, IPv6
Integration
Siloed — standalone systems
Cross-domain, multi-system collaboration
Example
Smart meter → utility server
Smart meter + grid + user app + pricing
KEY INSIGHT: IoT evolved FROM M2M — broader scope, open standards, intelligence & analytics

## Slide 5
SDN — Software Defined Networking for IoT
APPLICATION LAYER
IoT business apps define network behaviour & policies
(Traffic management, security, QoS)
CONTROL LAYER (SDN Controller)
Centralised brain — makes routing decisions, manages network state
(OpenDaylight, ONOS, Floodlight)
INFRASTRUCTURE LAYER (Data Plane)
Physical switches/routers — forward packets as instructed
(OpenFlow-enabled switches)
▼ Northbound API
▲ Southbound (OpenFlow)
▼ Northbound API
▲ Southbound (OpenFlow)
Benefits for IoT
Centralised Control
One controller manages all IoT devices
Programmability
Change network behaviour via software
Dynamic Traffic
Prioritise sensor vs video IoT data
Scalability
Add thousands of IoT devices easily
Security
Isolate compromised devices instantly

## Slide 6
NFV — Network Function Virtualization for IoT
VNF
Virtual Network Function
Software implementation of a network function
(virtual firewall, virtual router, virtual NAT)
NFVI
NFV Infrastructure
Standard servers + hypervisors providing compute, storage & network resources on which VNFs run
MANO
Management & Orchestration
Manages VNF lifecycle — deployment, scaling, monitoring, termination
SDN vs NFV — Quick Comparison
Aspect
SDN
NFV
Focus
Network control & management
Network function implementation
What it does
Separates control from data plane
Virtualises network functions (firewall, LB)
Benefit
Programmable, centralised control
Replace costly hardware with software
SDN + NFV together = agile, scalable, cost-effective IoT networks

## Slide 7
Sensors — The "Sense Organs" of IoT
Sensor: Measures a physical quantity and converts it to a digital signal for processing
Temperature
Smart thermostats, cold chain monitoring
Humidity
Greenhouse control, HVAC, weather
Pressure
Tyre pressure, barometric, blood pressure
Motion / Accel
Security systems, fitness trackers, drones
Light / Optical
Smart lighting, plant growth monitoring
Proximity
Smart parking, robot navigation, level sensor
Gas / Chemical
Air quality, CO detector, smoke detector
GPS / Location
Fleet tracking, asset management, navigation
Biometric
Heart rate, ECG, blood glucose monitor

## Slide 8
Actuators & MEMS
ACTUATORS — by Energy Type
Actuator: Converts digital/electrical signal → physical action
Electrical / Electromagnetic
Motors, solenoids, relays, electromagnets
Hydraulic
Hydraulic cylinders, motors (heavy machinery)
Pneumatic
Pneumatic cylinders, air valves, grippers
Thermal / Bimetallic
Thermostats, shape-memory alloys
Piezoelectric
Inkjet printer heads, micro-pumps, ultrasonic
Optical / Photonic
LEDs, laser diodes, LCD displays
MEMS
Micro-Electro-Mechanical Systems
Sensors + Actuators + Electronics on ONE silicon chip using microfabrication — measured in micrometres
Smartphone
Accelerometer, gyroscope, microphone, barometer
Car Airbag
MEMS accelerometer triggers airbag on impact
Fitness Tracker
MEMS accel, gyro, heart rate sensor
Inkjet Printer
MEMS micro-pump for precise ink control
Drones/UAVs
MEMS IMU — accelerometer + gyro + magnetometer
Key Advantage: Tiny, cheap, low-power — mass producible like microchips

## Slide 9
Smart Objects — The Building Blocks of IoT
Smart Object = Processor + Sensor(s)/Actuator(s) + Communication + Power
Processing Unit
Brain — processes sensor data, runs control logic
Microcontroller (Arduino, ARM Cortex-M)
Sensors / Actuators
Interface with physical world — sense and act
Temperature sensor + relay switch
Communication
Connects to network and other smart objects
WiFi, ZigBee, Bluetooth, LoRa module
Power Supply
Energy source for the device
Battery, solar cell, wired power
5 Trends in Smart Objects:
Smaller Size
Lower Power
More Processing Power
Better Communication
Increasing Standardisation

## Slide 10
Wireless Sensor Networks (WSNs)
Sensor
Node
Sensor
Node
Sensor
Node
Router /
Relay
Router /
Relay
Gateway /
Coordinator
Internet
Cloud
Server /
Application
FFD (Full Function Device)
Can be coordinator, router, or end device. Implements full protocol stack.
RFD (Reduced Function Device)
End device only. Talks only to FFDs. Simpler, cheaper, lower power — ideal for leaf sensor nodes.
Limited Processing
Limited Memory
Lossy Links
Low Data Rate
Limited Power

## Slide 11
WSN — Communication Patterns & Data Aggregation
EVENT-DRIVEN
Transmit ONLY when a specific event or threshold is detected
✓ Saves energy — ideal for alarms & alerts
Example: Motion sensor transmits only when motion detected
CO detector alerts only when CO > safe threshold
PERIODIC
Transmit at fixed time intervals regardless of conditions
✓ Predictable behaviour — ideal for monitoring
Example: Temperature sensor reports every 60 sec
Heart rate monitor reports every 5 minutes
VS
Data Aggregation
Cluster head collects readings from nearby nodes → computes aggregate (average, min, max) → sends ONE value upstream.
Reduces transmissions dramatically. Saves energy. Enables edge/fog processing.
Self-Organisation in WSNs:
Self-Configuration
Self-Healing
Self-Protection
Self-Optimisation

## Slide 12
Communication Protocols for WSNs
APPLICATION
CoAP, MQTT, HTTP
TRANSPORT
UDP (preferred — lightweight)
NETWORK
IPv6 / 6LoWPAN, RPL
DATA LINK / MAC
IEEE 802.15.4 MAC, CSMA/CA
PHYSICAL
IEEE 802.15.4 PHY (2.4GHz, 868/915 MHz)
← Protocol Stack (WSN)
IEEE 802.15.4
Foundation standard. 250 Kbps at 2.4 GHz. Short range (10–100m). Low power. Base for ZigBee/6LoWPAN.
ZigBee
Self-healing mesh. Up to 65,000 nodes. AES-128 security. Smart home & building automation.
6LoWPAN
IPv6 over 802.15.4. Compresses 40-byte IPv6 headers to 2 bytes. Enables end-to-end IP on constrained devices.
RPL
IPv6 routing for LLNs. Builds DODAG tree from sensors to gateway. IETF RFC 6550. Energy-efficient routing.
CoAP
RESTful protocol over UDP. Only 4-byte header. Request-response model like HTTP but ultra-lightweight.
MQTT
Publish-subscribe messaging. 2-byte fixed header. Ideal for telemetry over lossy, low-bandwidth networks.

## Slide 13
Connecting Smart Objects — Communication Criteria (Part 1)
RANGE
PAN — Personal Area (~1–10m)
Bluetooth, NFC, ZigBee
Wearable → smartphone
HAN — Home Area (~10–100m)
ZigBee, BLE
Smart home sensors
NAN — Neighbourhood (~100s m)
ZigBee mesh, 802.15.4g
Smart meters
FAN — Field Area (100m–few km)
LoRaWAN, 802.15.4g, LTE-M
Smart grid district
WAN — Wide Area (km+)
Cellular (4G/LTE), LoRaWAN, NB-IoT
Vehicle tracking
FREQUENCY BANDS
Licensed Spectrum
Allocated exclusively to licensed operators.
Costs billions. No interference.
Technologies: Cellular, WiMAX, NB-IoT
Unlicensed ISM Bands
868 MHz
Europe/India — better penetration, longer range
915 MHz
Americas/Australia — similar advantages
2.4 GHz
Worldwide — higher rate, more interference
Sub-GHz: Better penetration, longer range, lower data rate — PREFERRED for IoT

## Slide 14
Communication Criteria (Part 2) — Topology, Power & Constrained Devices
STAR
All devices connect to central hub/gateway.
Simple, low latency.
Single point of failure.
Used: WiFi, LoRaWAN, NB-IoT
MESH
Each device talks to multiple neighbours. Data hops through network.
Self-healing, extended range.
Used: ZigBee, Thread, WiFi mesh
PEER-TO-PEER
Any device talks directly to any other in range.
Flexible, no controller needed.
Limited range.
Used: Bluetooth, early ZigBee
POWER CONSUMPTION
Powered Nodes
Mains power — no constraint. Smart meter, industrial sensor
Battery (Sleep Modes)
1–10 years with deep sleep. ZigBee, parking sensor
Energy Harvesting
Indefinite. Solar/vibration. Smart agriculture sensors
Constrained Devices (RFC 7228)
Class 0
<10 KB RAM, <100 KB ROM
Pre-configured; no IP stack
Class 1
~10 KB RAM, ~100 KB ROM
Supports CoAP, lightweight protos
Class 2
~50 KB RAM, ~250 KB ROM
Can support more complex protocols

## Slide 15
Communication Criteria (Part 3) — Data Rate, Latency & Overhead
DATA RATE SPECTRUM
Sigfox
100 bps
LoRaWAN
300 bps–50 Kbps
NB-IoT
~200 Kbps
ZigBee
250 Kbps
LTE-M
~1 Mbps
WiFi
Up to 300 Mbps
LATENCY
Industrial robot control
< 1 ms — deterministic
Deterministic Ethernet / TSN
Smart grid protection
< 4 ms (IEC 61850)
802.15.4e TSCH
Patient monitoring alert
< 1 second
LTE-M, WiFi, ZigBee
Smart meter reading
Minutes acceptable
NB-IoT, LoRaWAN
OVERHEAD & PAYLOAD
IoT sensors send tiny payloads (2–4 bytes) — protocol overhead must be minimised:
IPv6 Header
40 bytes
Too large for 2-byte payload
6LoWPAN Header
2 bytes
Compressed IPv6 — perfect for WSN
HTTP Header
100s bytes
Far too heavy for IoT sensors
CoAP Header
4 bytes
Ultra-light REST over UDP
MQTT Fixed Header
2 bytes
Minimum overhead for pub-sub
LoRaWAN Payload
19–250 bytes max
Small payload by design

## Slide 16
Module 2 — Quick Revision
M2M
Machines talk directly, no humans — closed, proprietary
IoT
Broader, open, IP-based, intelligent analytics, scalable
SDN
Control plane (software) separate from data plane (hardware)
NFV
Network functions as software on COTS servers — not hardware
Sensor
Physical quantity → digital signal (INPUT to IoT)
Actuator
Digital signal → physical action (OUTPUT from IoT)
MEMS
Sensors + actuators + electronics on ONE tiny silicon chip
Smart Object
Processor + Sensor/Actuator + Comms + Power
WSN
Network of motes with coordinator/gateway to Internet
FFD
Full Function Device — coordinator, router, or end device
RFD
Reduced — end device only, simpler, cheaper, lower power
6LoWPAN
IPv6 compressed for 802.15.4 — 40 bytes → 2 bytes

## Slide 17
MODULE 2
Thank You
IoT and M2M • SDN & NFV • Smart Objects • WSNs • Communication Criteria
M2M & IoT vs M2M
SDN & NFV for IoT
Sensors & Actuators
MEMS & Smart Objects
WSN Architecture
WSN Protocols
Comm Criteria
PEMRT525 | KTU | S5 | JECC
Textbooks: Cisco Press IoT Fundamentals • Bahga & Madisetti